## Slide 1: CS101
Home Network Basics

## Slide 2: Computers love bytes and a factor of 1024
Up to now we have been using bytes as our main unit of measurement with a factor of 1024
For instance storage measured in bytes
  1 bit = 0 or 1
  1 bit * 8 = 8 bits = one byte
  1 byte * 1024 = 1024 bytes = 1 Kilobyte
  1 byte * 1024 * 1024 = 1,048,576 bytes = 1 Megabyte
  1 byte * 1024 * 1024 * 1024 = 1,073,741,824 bytes = 1 Gigabyte
  1 byte * 1024 * 1024 * 1024 * 1024 = 1,099,511,627,776 bytes = 1 Terabyte

## Slide 3: Networks Love Bits and a Factor of 1000
Movement measured in:
bits per second (bps)
  bps = How many bits go by a point in one second
  Also called Data Transmission Rate
1 bps = 1 bit per second
1bps*1000 = 1000bps = 1 kilobit per second = 1 kbps
1bps*1000*1000 = 1,000,000bps = 1 megabit per second = 1 Mbps
1bps*1000 *1000*1000 = 1,000,000,000bps = 1 gigabit per second = 1 Gbps
Etc

## Slide 4: Test your speed often!
ISP’s will happily charge you for speeds you are not getting
Google “Speed Test”
Try and test with direct (Ethernet cable) connection to router
Test at different times
Complain to ISP if not getting promised speed

## Slide 5: What is a network?
Network = Devices connected together so that they can exchange information

## Slide 6: A (home) network needs 3 things
Network Software
  Instructions to move information between devices
Protocols
  Agree upon way to do things
Connection
  Way to move information between devices

## Slide 7: Home Network Software
Built into the operating system
To see network settings:
  Windows = Start menu > Network and Internet
  Macintosh = Apple menu > System Preferences > Network

## Slide 8: Home Network Protocols
Handled by the networking software
Since everyone wants their network to be able to communicate with everyone else's network we all use the same protocols
To be part of the Internet you need to use the TCP/IP protocols = Transmission Control Protocol/ Internet Protocol
    Example = http = Hyper Text Transfer Protocol to move web pages around in an agreed upon way

## Slide 9: Home Connection = A Device Needs a NIC or a NI
To connect a device to a network it needs a:
  NIC = Network Interface Controller (or Card)
    or a
  NI = Network Interface
A NIC or NI allows a device like a computer, printer, scanner, etc, to connect to a network
Good to know because every NIC and NI has a MAC address
  Media Access Control address
  Unique address for each item on a network
    Can be found in System Information under Network Adapter

## Slide 10
What is at the center of a typical home network?
  Router or Router/Modem = Smart device that takes a message in one port and only sends it out the port that is connected to the device that is suppose to get the message. It can send information between two different networks, such as, your home network and the Internet.
    Most routers have ports to plug in Ethernet cables and wireless for Wi-Fi.
What is a Wi-Fi home mesh network?
  Multiple Wi-Fi routers designed to work well with each other to eliminate wireless dead zones.
Home Connection – How do I connect all my devices?

## Slide 11: Get your own router!
Get your own router and save money not renting one from your ISP. Also, increase security by making you different from everyone else.
PC Websites Best Routers and Mesh Networks
Best Wireless Routers
    Best Wi-Fi Mesh Networks

## Slide 12: Home connection options
Wireless (Wi-Fi)
Wired

## Slide 13: Home connection options - Wireless
Wireless (Wi-Fi)
  802.11 + a letter used to tell you which version, now they will be numbered as 4, 5, 6 and 7 are the most current.
    Versions of Wi-Fi
    Later standards are better: more range, faster, better security
A wireless router radios the information to devices on the network.
  Good to get router that broadcasts in more then one frequency i.e. 2.4Ghz and 5Ghz.

## Slide 14: The only way to know is verify encryption is being used!
Password is not proof you are encrypted.
Proof is in Network settings look for…
  WPA3- ASE

## Slide 15: If you go wireless…
Password Protect Router
  Change default password of router
Make sure wireless encryption is on and create good password
    WEP = Not quite as bad as nothing
    WPA = Bit Better
    WPA2 = Even A Bit Better
    WPA3 = Currently the best.
Use ASE not TKIP
Think about MAC address filtering and other options.
  Ready wireless router manual

## Slide 16: Home network connection options
Wired
  Ethernet cables
    Fast Ethernet 10Mbps/100Mbps
    Gigabit Ethernet 10Mbps/100Mbps/1000Mbps
  Power Line Networking (electrical system)
  Phone Line Networking (phone system)

## Slide 17: What do you have when you have setup your home network?
You have a L.A.N
LAN = Local Area Network = All the equipment is in the same physical area

## Slide 18: What do you have when you hookup some LAN’s in the same city?
You have a M.A.N
MAN = Metropolitan Area Network = LAN’s hooked together in the same city

## Slide 19: What do you have when you hookup some LAN’s in different cities?
You have a W.A.N
WAN = Wide Area Network = LAN’s hooked together in the different cities

## Slide 20: What do you have when you hookup lots of LAN’s, MAN’s, and WAN’s?
You have the Internet
Internet = Refers to the equipment that makes up the biggest network in the world